Loom rental program

Table loom

12 shafts

Includes:

stand

warp extension kit

sectional warp beam kit

WhichOne kit

"Carolyn"

By

Woolhouse tools

http://www.woolhousetools.com/

| Carolyn 12 shafts, with overhead beater option | Margaret, 24 shafts, top front |
| --- | --- |

Our Carolyn and Margaret table looms, all models 23" weaveable, show delightfully smooth action because all cords run over pulleys--never dragged over rods or through eyes.  White rubber feet protect table tops.  Shaft control keys and warp and cloth winding controls are where they're easiest to reach--front and center and out in the open.  Double pawls, back and front, make 36 stops per beam turn.

Margaret's shafts 9 through 16 or 24 open sheds as fully as shaft 8, the same shed opening on our Mimi and Carolyn looms, a shed more than adequate for most boat shuttles.  Three beater positions allow optimum beater placing.  An optional overhead beater option beats your fell line at 900.

Carolyn and Margaret looms are supplied with a pair of lease sticks, two flat shuttles, one reed - 6, 8, 10, 12, 15, or 20 d.p.i., 400 7" heddles for the Carolyn 4s and 8s, 600 7" for the Carolyn 12s, 800 10.5" for the Margaret 16s, and 1200 10.5" for the Margaret 24s.

All Carolyn and Margaret looms have an overall width of 30".  Weaving mode overall height for Carolyn looms is 25", for Margaret looms, 27".  The front to rear depth for Carolyn looms is 29", for Margaret, 40".

The Carolyn 4s loom weighs 21.5 lb., the Carolyn 8s loom, 27.5 lb., the Carolyn 12s loom, 33.5 lb., the Margaret 16s, 45 lb., and the Margaret 24s, 55 lb.

| Weights and Measures for Woolhouse Tools Table Looms |
| --- |
|  | Weight | Width weaveable | Width Overall | Height overall, weaving mode | Depth overall, weaving mode | Height overall, flat fold | Stand, weight | Heddles supplied (length) |
| Carolyn, 12 shafts | 33.5 lb. | 23 in. | 30 in. | 25 in. | 29 in. | --- | 15 lb. | 600 (7") |

WhichOne

WhichOne places each repeat of a draft to within easy and quick eye-range of the loom keys.  After having set up the bars in accordance with the draft, pull keys as peg positions dictate.  Weave the pick.  Pull out the bottom bar and drop it on top.  The next pick keys are shown right there.

No re-focusing on a complicated draft.  No memory loss between seeing what you need and putting fingers to keys.

Supplied with bars, anchor pegs, and a bar holder for repeats up to 16 picks long.

Easily mounts on any Carolyn or Margaret loom.

| Mimi, 4 shafts, with our Folding Stand |  |
| --- | --- |

Shown in the photograph but not included with the PVW's Carolyn are a Tension Box and a Sectional Guide.

About Woolhouse Tools

All items with our Woolhouse Tools mark are designed and built in our workshop.  Apart from nuts and bolts hardware, the only parts we buy ready-made are springs, reeds, and Texsolv items.  Proprietors and the entire working staff are John and Teruko Low, helped occasionally by friends and relations.

Our wood is birch cut in the valleys of the North Okanagan hills nearby.  We ourselves choose our logs or standing trees, and hire fallers, sawyers, and truckers to carry home the timber we need to build our equipment.  We air dry the rough wood under roofs outside, one year per inch of thickness, and then mill it ourselves.

We study our designs and other maker's designs constantly, always looking to build you, our customers, the best weaving and spinning tools found anywhere, at the most reasonable prices.

Our workshop and showroom are on our country acreage about five hours drive northeast of Vancouver, B.C.  We do welcome visits by those interested in our equipment, but visitors should call in advance.  We can be away to a weaver's convention, or busy in the garden, our summer indulgence.

Our simple guarantee is this: if you are unsatisfied with what you purchase and return the goods within sixty days, we will refund all you have sent us.